## Slide 1: Networked Radiation
Low Cost, designed for production, radiation, and weather sensor.

## Slide 2: Current market options
Portable Geiger counters
Weather stations
Computer with USB sensors
Conglomerating multiple sensors with a common hub
Notes: Most sensors are designed for a single unit, and are bulky and draw high amounts of power to run auxiliaries.
Whether stations come at high cost and are similar large because of casings.

## Slide 3: Sensor Requirements
Be designed for manufacturing
Low Power Consumption
RF transmitting (FCC/ISM)
Multiple Transmitter, Single Reciver, Error Checking
Strong Casing
Easy Mounting
Weatherproof
Documented code and hardware
Notes: Part cost in bulk, part availability, PVC Pipe, and magnets?

## Slide 4: Transmitter Software
Pin Change Interrupt
Sensor Readings
Encode Data with ID
Transmit Data
Sleep

## Slide 5: Transmitter Hardware
Micro Controller
Temperature
RF Transmitter
Humidity
Charging Circuit
Solar Cell
Battery
Geiger Tube
HV Supply
Pressure
PCB antenna

## Slide 6: Receiver Software
Arduino RF input
OS Level now, Can do anything
Graphing
Location Processing
SQL
Server Storage
Decode bits into data, Serial Print

## Slide 7: Receiver Hardware
Antenna
RF Receiver
Arduino
USB (HID/COM)

## Slide 8: Microcontroller Selection
Most program in C
AVR is higher performance/ clock cycle
AVR can be forced to take Arduino code.
8 pin variant 1k memory enough for needs
Down to 16nA when sleeping
Available in SMD Package.

## Slide 9: Transmitter and Receiver
Using ISM (Industrial, Scientific, Medical) open band for communication.
  A lot of noise form other devices
  100mW max power at antenna
  315MHz, 433MHz, 915MHz, 2.4GHz, 5GHz, 60Ghz…
  Lower frequency for better penetration, but lower data rate.
  315MHz not recommenced (4th harmonic of gps)
  Manchester encoding
  PCB antenna cheapest, yet still effective
  Theoretical 100M range